Important topics and commands to practice from unix/linux:-

LINUX Features
File system
Architecture of linux (“kernel”) command : uname -a

=======
“ls” command and all its combinations like
ls -l ,ls -ls, ls -al, ls -h,...etc
syntax:-ls options fielname
cd	(change directory) cd –	cd ~
“mkdir” to create a directory
mkdir -p
practice this command by making single and multiple directories at a time
syntax:-mkdir dirname
“cp” command to copy different files and folders from source to destination
syntax:-cp source/path target/path
“mv” command to rname or move file from one folder to another
syntax:-mv filename target/path(to move)
mv oldfilename newfilename(to rename)
“more” command to display file contents page by page
syntax:-more filename
“less” command is same as more but with some extra feature so that we can scroll up and down
syntax:-less filename
alias – used to set set alias names
“echo” command it prints whatever given next to that command on the terminal
synatx:-echo myname
output:-myname

File Permission Commands::----

“chmod” command to change permissions on file,it has two method
1)chmod octal filename (numbers are given in place of octal)
2)chmod symbolic filename(here characters are given in place of symbolic)
references:-
r-->user
g-->group members
o-->other users
a-->all users
operators:-
“+” to add specific file permissions
“-” to remove specific file permission
“=” to add the bits
modes:--
r-->read
w-->write
x-->execute
s-->set uid or guid ,other commands for changing file permission are(chattr, setfattr, setfacl , setcap)
“umask” used to change default file permissions
id – to know effective user and group id's
File -determibnes file types
“chgrp” to change group	syntax:-chgrp groupname
“head” command to view top lines from a file
syntax:-head <n> filename
n=no.of lines
“tail” command to view lines from bottom
and tail is also used monitor log files
syntax:-tail <n> filename
head & tail combination with pipe
“find” command to find files and folders in the directories
find -name, find -size , find -perm , find -type , find | exec
syntax:-find dirtosearchfrom -name filename
“locate” command to locate a particular file types
syntax:--locate “.txt”
locate “.docs”
“grep(general regular expression)” command to look for a particular pattern
syntax:--grep options pattern files
options== -c,-v,-i,-n
combination of find and grep commands
“tar” command to backup files and folders in archive format
syntax:--tar options filename
“compress or gzip” command to compress file
gzip filename
gzip -d filename (to unzip)
All the file compression and file extraction commands and its combination
“mount” command to mount a media device (ex:-cdrom,floppydrive)
“jobs” command to see the no of jobs running
“ps” to see the processess going on present
“top” to snapshot linux tasks with resources like memory,cpu…..
free , du , df –are about system memory
“kill” to kill the process which are running
netstat – network statistics
netstat – l and with grep combination to know about particular port
“telnet” to connect to other machines
“ssh” to connect to other machines but this is a secure connection
syntax::-ssh root@hostipaddres
who , who am I , whoami -shows who is logged on
“ping” to check the status of the hostmachine
wget- network downloader
“scp(secure copy)” to copy from host/client to client /host
“sed” its a stream editor to edit the txt file
“awk” to print a selected number of columns from a file having column format data
“man” it is command to see manual pages of the other commands its like a user manual
“info” it gives info on the command in a summarized format
“help” its a help tool
cat – to create file and add , append data to a file
diff, sdiff - to compare to files
touch – to create a file
“vi” this command is used for editor “vi” is a txt editor
gg , G , (5,6t10) , a ,A ,o ,O ,i , I find and replace
syntax:-vi filename
***even if the file dosnt exist it will creat a new one***
all the references of vi editor
“su” to switch user
syntax:-su username
**if u dont specify user it will take it as root then u have to enter password for that user**

“useradd” to add a user
syntac:-useradd username
password

“groupadd” to create a group
syntax:--groupadd options groupname

“usermod” to change user account settings and it is used by administrator

crontab- to shedule a command or script
crontab -l , crontab -e